Round Chopstick Machine Production Line

1.Raw Bamboo Sawer

| Item No. | BCM 001 |  |
| --- | --- | --- |
| Power | 1.5 KW |  |
| Saw Diameter | Ø 400 MM |  |
| Axis Speed | 3200R/MIN |  |
| Weight | 50 KG |  |
| Size | 870×540×1340MM |  |

2.Bamboo Splitting Machine

| Item No. | BCM 002 |  |
| --- | --- | --- |
| Power | 5.5 KW |  |
| Output | 250,000 KGBamboo/Day |  |
| Mechanical Size | 4250×900×1110 MM |  |
| Weight | 620 KG |  |

3.Fixed Width Slicer

| Item No. | BCM 003 |  |
| --- | --- | --- |
| General Power | 9.0 KW |  |
| Main Axis Speed | 3000 R/MIN |  |
| Knive Diameter | ø 80 |  |
| Thickness it procesess | 5~46 MM |  |
| Kinve Equipped | 2 SETS |  |
| Width it processes | 15~~30 MM |  |
| Feeding Speed | 75 M/MIN |  |
| Weight | 850KG |  |
| Mechanical Size | 2300×780×1130MM |  |

4.Bamboo Wool Slicer

| Item No. | BCM 004 |  |
| --- | --- | --- |
| Power | 9.5 KW |  |
| Main Axis Speed | 2800R/MIN |  |
| Output | 2500 KG BAMBOO |  |
| Feeding Speed | 55~~75 M/MIN |  |
| Weight | 455 KG |  |
| Mechanical Size | 1280×1020×1170 MM |  |

5.Chopstick Precise Cutter

| Item No. | BCM 005 |  |
| --- | --- | --- |
| Saw Quantity | 3 PCS |  |
| Saw Diameter | Ø300 |  |
| Saw Speed | 3200R/MIN |  |
| Weight | 64 KG |  |
| Mechanical Size | 670×680×840MM |  |

6.Chopstick Polishing Machine

| Item No. | BCM 006 |  |
| --- | --- | --- |
| Main Axis Speed | 160 RPM |  |
| Cubage Inside | 0.3 M3 |  |
| Weight | 166 KG |  |
| Size | 2400×880×830MM |  |

7.Chopstick Shape-Former

| Item No. | BCM 007 |  |
| --- | --- | --- |
| General Power | 2.25 KW |  |
| Output | 200~220 Pairs/MIN |  |
| Axis Speed | 3860 R/MIN |  |
| Size | 1450×880×830MM |  |
| Weight | 210 KG |  |

8.Blade Sharpener

| Item No. | BCM 008 |  |
| --- | --- | --- |
| General Power | 0.37 KW |  |
| Kinve Diameter | Ø80~~ Ø160 |  |
| Main Axis Speed | 2800 R/MIN |  |
| Alloy Sander Dia | Ø160 |  |
| Weight | 60 KG |  |
| Mechanical Size | 450×350×660 MM |  |

9.Toothpick Packing Machine

| Item No. | BCM 009 |  |
| --- | --- | --- |
| General Power | 0.25 |  |
| Length it can pack | 65--70MM |  |
| Output | 200~220 Bag/Min |  |
| Weight | 500 KG |  |
| Mechanical Size | 1500×600×1600 MM |  |

Payment: 50% T/T in advance, balance before shipment.

Packing: Wooden Case

Delivery: Within 40 days after receiving the deposit.

The above productionline is very suitable for the bamboo in Vietnam, Indonesia,

Thailand, India, etc.

Our bank information:

PLEASE PAY TO:

HANGZHOU GARDEN TRADING CO.,LTD.

THE AGRICULTURAL BANK OF CHINA ZHEJIANG BRANCH,HANGZHOU,ZHEJIANG,CHINA

SWIFTBIC:ABOCCNBJ110

USD A/C NO.:302-048101040011330

Remarks: Our products are under improving and if the final product apprearane is different in picture and design, the final products are regarded as the standard. Hoping you could understand.

Efficiency: 96,000 pairs / 8 hours.

How to Contact Us?

Hangzhou Garden Trading Co., Ltd.

Contact Person:

Angel Zhou

Tel:0086 571 28057068

Fax: 0086 571 28928911

Mobile: 0086 139 5710 6971

Email: angel@gardenchem.com

MSN: Angelzhou1224@hotmail.com

Skype: angel12242008

Add: 7F, Sanxin Mansion, No.35 Xintang Road, Hangzhou, China